## Slide 2
QMK/VIA/VIAL FIRMWARE FLASHING MANUAL
If your keyboard runs on QMK firmware, this tutorial is for you.
If a new firmware version is available for your keyboard, you can upgrade it using the QMK Toolbox software. After the firmware upgrade, your keyboard settings will be reset to default values.
Here is a step-by-step guide on how to perform the firmware upgrade.
Download the latest firmware for your keyboard. Firmware file should have a .bin extension.
Please carefully check that you have downloaded the firmware specifically for your model.
Step 1
Download and install QMK Toolbox
Windows: https://github.com/qmk/qmk_toolbox/releases/latest/download/qmk_toolbox_install.exe
macOS: https://github.com/qmk/qmk_toolbox/releases/latest/download/qmk.toolbox.app.zip
Step 2
Run QMK Toolbox as administrator.
Step 3

## Slide 3
This step is required only for Windows systems.
Click on the “Tools” tab and select “Install Drivers”.
Step 4
Wait until the process completes.
Confirm the driver installation.

## Slide 4
Put the keyboard in firmware upgrade mode
To do this:
1. ⚠️ If your keyboard is wireless, first switch it to wired mode using the toggle switch on the case.
2. Disconnect the USB cable from the keyboard (if connected).
3. Press and hold the ESC key.
4. While still holding the ESC key, plug the USB cable back into the keyboard.
Step 5
If the drivers were installed correctly, you will see a yellow text message indicating that the device is connected.

## Slide 5
Click the “Open” button and select the downloaded keyboard firmware file.
Step 6

## Slide 6
Click the “Flash” button and wait until the process completes.
DO NOT UNPLUG YOUR KEYBOARD DURING THIS PROCESS!
You should see a yellow “Flash complete” message without any errors or warnings.
Step 7
You can now disconnect and reconnect your keyboard — the firmware update is complete.
If the flashing process fails, try repeating steps 5-8.
Step 8